## Slide 1: Boolean Algebre
Lecture 2
Prepared by : Eng.Amani Safwat

## Slide 2
Boolean Algebra is a branch of mathematics for digital logic
Founded by George Boole
Used in computers and digital systems
Introduction

## Slide 3
Variables (A, B, C…..) → Its value is 0 or 1
AND (·)
OR (+)
NOT (′)
Basic Symbols

## Slide 4
Identity Law: A+0=A , A·1=A
Null Law: A+1=1 , A·0=0
Idempotent Law: A+A=A , A·A=A
Complement Law: A+A′=1 , A·A′=0
Commutative Law : A+B=B+A , A.B = B.A
Associative Law : A+B+C=(A+B)+C , A.B.C=(A.B).C
Distributive Law : A.(B+C)=A.B+A.C , A+(B.C)=(A+B).(A+C)
De Morgan’s Theorem : (A+B)`=A`.B` , (A.B)`=A+B`
Basic Laws

## Slide 5
EX 1:
F = A + AB
We take out a common factor
A (1+B) => 1+B=1
So F =A
EX 2 :
F = AB + AB`
A(B +B`) => B+B`=1
So F =A
Example

## Slide 6
EX 3:
F = A (A`+B)
AA` +AB =>A.A`=0
So F=AB
EX 4 :
F= AB+BC(B+C)
AB+BBC+BCC
AB +BC +BC
B(A+C)
So f= B(A+C)
Example

## Slide 7
EX 5:
F = AA+AC+AB+BC
A+AC+AB+BC
A(1+C+B)+BC
So F= A+BC
Example

## Slide 8
EX 6 :
AB+A(A+C)+B(A+C)
AB +AA+AC+AB+BC
AB+A+AC+BC
A(B+1+C)+BC
So F = A +BC
Example

## Slide 9
EX 7:
F = ( ( (CD)` +A`)` +( (C` D + A`))`
= C`+D`+A . (C+D`) .A
=(C` +D` +A) . (AC+AD`)
=ACC`+ACD` + AAC +AD`C`+A D`D`+ AAD`
=ACD` + AC +AD`C`+ AD`
=AC(D`+1)(AD`C+AD`)
=AC+AD`(C+1)
=AC+AD`
=A(C+D`)
Example

## Slide 10
Thank you