## Slide 1: Karnaugh map
Lecture 5
Prepared by : Eng.Amani Safwat

## Slide 2: Introduction
A Karnaugh Map (K-map) is a graphical method used to simplify Boolean functions by organizing all possible combinations of variables in a visual grid. It helps to minimize logic expressions without using complex algebraic steps, making digital circuit design more efficient. Each cell in the map represents a minterm (for SOP) or maxterm (for POS),.
In short: K-maps make it easier to find simplified logic equations by grouping 1s or 0s in patterns of

## Slide 3: Why Simplification
- To reduce the number of logic gates.
- To simplify circuit design.
- To save cost and power

## Slide 4: K-map Layouts
- 2-variable: 4 cells
- 3-variable: 8 cells
- 4-variable: 16 cells

## Slide 5: Karnaugh map
 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 0 | 0 | 1
 | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1
 | 0 | 1
0 | 0 | 0
1 | 1 | 1
2 inputs
3 inputs
4 inputs
A
B
AB
C
AB
CD
 GARY CODE
 GARY CODE
2n = n (1,2,3,4,…)
implicant

## Slide 6: Simplification Steps
1. Draw K-map
2. Fill cells with 1’s or 0
3. Group adjacent 1’s (1,2,4,8,…)
4. Write the simplified equation

## Slide 7: Two Variables
Apply the Karnaugh map to the following table:
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
 | 0 | 1
0 | 1 | 1
1 | 0 | 0
B
A
F= B’
=B’

1. F= A’B’ + AB’

A.

## Slide 8: Two Variables
Apply the Karnaugh map to the following table:
A | B | F
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
 | 0 | 1
0 | 1 | 0
1 | 1 | 0
B
A
F= A’
= A’

1. F= A’B’ + A’B
B.

## Slide 9: Three Variables
Apply the Karnaugh map to the following table:
A | B | C | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
F= A’ +C’
= C’

1.F=A’B’C’+A’B’C+A’BC’+A’BC+AB’C’+ABC’
2.

3.
 | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0
C
AB
=A’

## Slide 10: four Variables
Apply the Karnaugh map to the following table:
F= BC’D+B’D’ +AB’C’

3.
 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 0 | 1 | 1 | 1
11 | 0 | 0 | 0 | 0
10 | 1 | 0 | 0 | 1
AB
CD
1.F=A’B’C’D’+A’B’CD’+A’BC’D+AB’C’D’ +AB’C’D +AB’CD’ + ABC’D
2.
AB’C’
B’D’
BC’D

## Slide 11: Exercise
Apply the Karnaugh map to the following table:
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1

## Slide 12: Answer
Apply the Karnaugh map to the following table:
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
 | 0 | 1
0 | 1 | 1
1 | 0 | 1
B
A
F= A’B’ + AB’ + AB= >A+B’
So F = A+B`
=B’
1. F= A’B’ + AB’ + AB
=A