## Slide 1: Logic Design - Introduction
Prepared by : Eng.Amani Safwat

## Slide 2
Logic Design is a branch of computer engineering that uses logic circuits to process binary data (0s and 1s).
What is Logic Design?

## Slide 3
To create RAM (CPU): the cores that execute every instruction in a computer.
To create memory: the place where the ones and zeros are stored.
To create any digital device: such as phones, controllers, and smart cars.
Why do we need logical design?

## Slide 4
Number Systems
Decimal (10) : 0-9 “used by humans”
Binary (2) :0-1 “used by computers”
Octal (8) :0-7 “shortcut for binary”
Hexadecimal (16):0-9 A-F “used in programming”
A = 10 , B = 11 , C =12 , D = 13 , E = 14 , F = 15

## Slide 5
Mapping

## Slide 6
Binary Systems
• Represented: 0,1
Mapping from binary to decimal:
Weights method :
2 n = m 2 0 =1 2 1 =2 2 2 =4 2 3 =8 2 4 =16 2 5 =32
EX:
(110110)2 ->(?)10
32 16 8 4 2 1
1 1 0 1 1 0
We collect what is above one
32+16+4+2=54
So (110110)2 ->(54)10

## Slide 7
Binary Systems
Mapping from binary to Octal :
We divide the number into 3 digits then We collect what is above one
EX:
(10010)2 ->(?)8
0 1 0 0 1 0
4 2 1 4 2 1
2 2
So (10010)2 ->(22)8

## Slide 8
Binary Systems
Mapping from binary to Hexadecimal :
We divide the number into 4 digits then We collect what is above one
EX:
(111010)2 ->(?)16
0 0 1 1 1 0 1 0
8 4 2 1 8 4 2 1
3 A
So (111010)2 ->(3A)16

## Slide 9
decimal Systems
Mapping from decimal to Binary :
We use the weights method, and the last number is the smallest and closest number to the decimal number. Then we make one for the numbers that are equal to the decimal number, otherwise zero.
EX:
(55)10 ->(?)2
32 16 8 4 2 1
1 1 0 1 1 1
So (55)10 ->(110111)2

## Slide 10
decimal Systems
Mapping from decimal to Hexadecimal :
Convert from decimal to binary and from binary to Hexadecimal
EX:
(210)10 ->(?)16
10 ->2
128 64 32 16 8 4 2 1
1 1 0 1 0 0 1 0
2 ->16
1 1 0 1 0 0 1 0
8 4 2 1 8 4 2 1
D 3
So (210)10 ->(D3)16

## Slide 11
decimal Systems
Mapping from decimal to Octal :
Convert from decimal to binary and from binary to Octal
EX:
(22)10 ->(?)8
10 ->2
16 8 4 2 1
1 0 1 1 0
2 ->8
0 1 0 1 1 0
4 2 1 4 2 1
2 6
So (22)10 ->(26)8

## Slide 12
Octal Systems
Mapping from Octal to binary :
EX:
(67)8 ->(?)2
6 7
4 2 1 4 2 1
1 1 0 1 1 1
So (67)8 ->(110111)2

## Slide 13
Octal Systems
Mapping from Octal to decimal :
Convert from Octal to binary and from binary to decimal
EX:
(43)8 ->(?)10
8 ->2
4 3
4 2 1 4 2 1
1 0 0 0 1 1
2 ->10
32 16 8 4 2 1
1 0 0 0 1 1
32+2+1+35
So (43)8 ->(35)10

## Slide 14
Octal Systems
Mapping from Octal to Hexadecimal :
Convert from Octal to binary and from binary to Hexadecimal
EX:
(36)8 ->(?)16
8 ->2
3 6
4 2 1 4 2 1
0 1 1 1 1 0
2 ->16
0 0 0 1 1 1 1 0
8 4 2 1 8 4 2 1
1 E
So (36)8 ->(1E)16

## Slide 15
Hexadecimal Systems
Mapping from Hexadecimal to binary :
EX:
(AFF)16 ->(?)2
A F F
8 4 2 1 8 4 2 1 8 4 2 1
1 0 1 0 1 1 1 1 1 1 1 1
So (AFF)16 ->(101011111111)2

## Slide 16
Hexadecimal Systems
Mapping from Hexadecimal to decimal :
Convert from Hexadecimal to binary and from binary to decimal
EX:
(AC)16 ->(?)10
16 ->2
A C
8 4 2 1 8 4 2 1
1 0 1 0 1 1 0 0
2 ->10
128 64 32 16 8 4 2 1
1 0 1 0 1 1 0 0
128+32 +8+4=172
So (AC)16 ->(172)10

## Slide 17
Hexadecimal Systems
Mapping from Hexadecimal to Octal :
Convert from Hexadecimal to binary and from binary to Octal
EX:
(101)16 ->(?)8
16 ->2
1 0 1
8 4 2 1 8 4 2 1 8 4 2 1
0 0 0 1 0 0 0 0 0 0 0 1
2 -> 8
0 0 0 1 0 0 0 0 0 0 0 1
4 2 1 4 2 1 4 2 1 4 2 1
0 4 0 1
So (101)16 ->(0401)8