## Slide 1: Logic gates
Lecture 3
Prepared by : Eng.Amani Safwat

## Slide 2: Logic Gates
Logic gates are electronic circuits used to perform logical operations on binary signals (0 and 1).
They are the basic building blocks of digital circuits such as computers, processors, and embedded systems.

## Slide 3: Why We Use Logic Gates
We use logic gates to control the flow of signals within digital systems and to perform logical and arithmetic operations such as addition, comparison, and data storage. They form the foundation of all digital systems

## Slide 4: Types of Logic Gates
(Basic Gates):
AND Gate
OR Gate
NOT Gate
(Universal Gates):
NAND Gate
NOR Gate
(Special Gates):
XOR Gate (Exclusive OR)
XNOR Gate (Exclusive NOR )

## Slide 5: AND Gate
Outputs 1 only if all inputs are 1
Used when all conditions must be true
Symbol
Truth Table |  | 
A | B | Y
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
Equation :Y= AB OR Y=A.B

## Slide 6: OR Gate
Outputs 1 if at least one input is 1
Used when only one condition needs to be true.
Symbol
Equation :Y=A+B
Truth Table |  | 
A | B | Y
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1

## Slide 7: NOT Gate
Inverts the input; if input is 1, output is 0
Used to reverse logical states
Truth Table | 
A | Y
0 | 1
1 | 0
Symbol
Equation :Y=A

## Slide 8: NAND Gate
The output is 0 only if all inputs are 1 (inverse of AND).
Used as a universal gate to build any logic circuit.
Symbol
Equation :Y=AB
Truth Table |  | 
A | B | Y
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 9: NOR Gate
Symbol
Equation :Y=A+B
Truth Table |  | 
A | B | Y
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
Outputs 1 only when all inputs are 0 (inverse of OR).
Used as a universal gate to build any circuit

## Slide 10: XOR Gate
Symbol
Equation :Y=A B
Truth Table |  | 
A | B | Y
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Outputs 1 only when inputs are different
Used in adder and comparator circuits

## Slide 11: XNOR Gate
Symbol
Equation :Y=A B
Truth Table |  | 
A | B | Y
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
Outputs 1 only when inputs are the same
Used in equality comparator circuits

## Slide 12
Universal Gates

## Slide 13: NAND Gate
NOT using NAND:
Y = (A · A)′ → gives the same output as NOT.

## Slide 14: NAND Gate
AND using NAND:
Y = ((A · B)′)′ → We use two NAND gates.

## Slide 15: NAND Gate
OR using NAND:
Y = ((A′) · (B′))′ → We use three NAND gates.

## Slide 16: NOR Gate
NOT using NOR:
Y = (A + A)′ → Same result as NOT

## Slide 17: NOR Gate
OR using NOR:
Y = ((A + B)′)′ → We use two NOR gates

## Slide 18: NOR Gate
AND using NOR:
Y = ((A′) + (B′))′ → We use three NOR gates